## Slide 1: CONTRAIL-CONTROL Testing
Ananth Suryanarayana (Anantha@juniper.net), Contrail Engineering
https://github.com/rombie/contrail-misc/blob/master/ContrailController.pptx?raw=true
Juniper Networks Proprietary and Confidential -- printed copies of this document are for reference only

## Slide 2: CONTROL NODE ARCHITECTURE
Control Node
All Control Plane Nodes are active active
Each vRouter uses XMPP to connect with multiple Control Plane nodes for redundancy
Control Nodes implement the BGP Speaker
BGP is used to connect with Physical Gateway Routers or switches
Control Plane Nodes federate using BGP
Control Node
…
BGP
IF-MAP
Cassandra DB
…
XMPP
BGP
Compute Node
Compute Node
BGP
L2 / L3 GW
L2 / L3 GW
…
…
XMPP

## Slide 3: Control node – test driven development (tdd)
Unit testing using google-test framework
  Framework wiki -- Setup(), Test(), TearDown()
  Mock entire classes when necessary – Use Factory create
  Virtualize functions when necessary
  Use TASK_UTIL_EXPECT_* macros to retry and wait for test conditions verification
    Makes test more reliable
  Use TaskFire() to make test code run in any particular “scheduler task
  Test Parameterization
Sample unit test
  bgp_attr_test.cc
  bgp_mvpn_test.cc
  bgp_peer_close_manager_test.cc

## Slide 4: test driven development (tdd) Continued
bgp_stress_test – More of an integration test but still uses unit testing framework
  Wiki
  bgp_stress_test.cc
  E.g. build/debug/bgp/test/bgp_stress_test --pause --nevents=-1 --npeers=5 --nroutes=5 --nagents=5 --ninstances=5
  Introspect
Configuration load
  Load cassandra configuration directly into control-node like unit test
  E.g. DBLOG_DISABLE=1 CONFIG_JSON_PARSER_TEST_DATA_FILE=/cs-shared/db_dumps/workday.json CONFIG_JSON_PARSER_TEST_INTROSPECT=5910 controller/src/ifmap/client/testdata/cassandra_to_json.rb
  Introspect
  config_json_parser_test.cc
  cassandra_to_json.rb

## Slide 5: test driven development (tdd) Continued
Code coverage using gcov
  Sample Report for BGP
Profie using valgrind, zoom, etc.
  Sample interesting but that I found just last week while running an unit test

## Slide 6: COMPUTE NODE: vRouter, HYPERVISOR
vRouter Forwarding Plane
Routing Instance
(Tenant Blue)
Flow Table
Tap Interface (vif)
FIB
VM 1
(Tenant Blue)
Compute Node
Routing Instance
(Tenant Green)
Flow Table
FIB
Routing Instance
(Tenant Red)
Flow Table
FIB
VM 2
(Tenant Green)
VM 1
(Tenant Red)
VM 1
(Tenant Red)
…
eth 1
eth N
vRouter Agent
vRouter replaces the Linux Bridge or OVS module in Hypervisor Kernel
vRouter performs bridging (E-VPN) and routing (L3VPN)
vRouter performs networking services like Security Policies, NAT, Multicast, Mirroring, and Load Balancing
config
Policy Table
VRFs
Overlay Tunnels: MPLSoGRE / VXLAN / ...