## Slide 1: CONTRAIL CONTROL architecture
Ananth Suryanarayana (Anantha@juniper.net), Contrail Engineering
Juniper Networks Proprietary and Confidential -- printed copies of this document are for reference only

## Slide 2: CONTRAIL ARCHITECTURE ENABLES INTENT BASED NETWORKING
Physical IP Fabric (no changes)
CONTRAIL CONTROLLER
ORCHESTRATOR
Host O/S
vRouter
Network / Storage orchestration
Gateway
…
Internet / WAN or Legacy Env.
(Config, Control, Analytics, Svr Mgmt)
(Windows, Linux ….) on BMS
TOR
Compute orchestration
Virtual Network Blue
Virtual Network Red
FW
Logical View
…
Centralized
Policy Definition
Distributed
Policy Enforcement
BGP
BGP
XMPP
OVSDB
Notes: we have a Neutron Plugin which enables all the Neutron v2 APIs. – Config Node also enables a set of APIs such as which Neutron does not provide yet … e.g. Service chaining …
Through this plugin OpenStack can talk to the Controller module … where we have a logically centralized controller that integrates with OpenStack Neutron …
It federates control plane traffic with other controller instances using BGP – and that is how it scales the control plane …
The controller allows operators – through OpenStack – to define service policies … Which are enforced in the data plane … these virtual networks are created by leveraging L3VPN constructs and that helps customers connect these virtual networks and services to the L3VPN environment …
At the data plane level there is a vRouter (light-weight kernel loadable module) that runs on each host … these hosts could be servers in a data center or even CPE devices …
Provides overlay virtual networking using overlay tunnels … running across the hosts and to the TORs …
All the overlay tunnels terminate on the GW  and that takes the traffic either to the L3VPNs or to the Internet …
The Controller also talks to the TORs to configure bridge domains to connect the bare metal servers to virtual networks …

## Slide 3: CONTROL NODE ARCHITECTURE
Control Node
All Control Plane Nodes are active active
Each vRouter uses XMPP to connect with multiple Control Plane nodes for redundancy
Control Nodes implement the BGP Speaker
BGP is used to connect with Physical Gateway Routers or switches
Control Plane Nodes federate using BGP
Control Node
…
BGP
IF-MAP
Cassandra DB
…
XMPP
BGP
Compute Node
Compute Node
BGP
L2 / L3 GW
L2 / L3 GW
…
…
XMPP

## Slide 4: COMPUTE NODE: vRouter, HYPERVISOR
vRouter Forwarding Plane
Routing Instance
(Tenant Blue)
Flow Table
Tap Interface (vif)
FIB
VM 1
(Tenant Blue)
Compute Node
Routing Instance
(Tenant Green)
Flow Table
FIB
Routing Instance
(Tenant Red)
Flow Table
FIB
VM 2
(Tenant Green)
VM 1
(Tenant Red)
VM 1
(Tenant Red)
…
eth 1
eth N
vRouter Agent
vRouter replaces the Linux Bridge or OVS module in Hypervisor Kernel
vRouter performs bridging (E-VPN) and routing (L3VPN)
vRouter performs networking services like Security Policies, NAT, Multicast, Mirroring, and Load Balancing
config
Policy Table
VRFs
Overlay Tunnels: MPLSoGRE / VXLAN / ...

## Slide 5: Control node – test driven development (tdd)
Unit testing using google-test framework
  Framework wiki -- Setup(), Test(), TearDown()
  Mock entire classes when necessary – Use Factory create
  Virtualize functions when necessary
  Use TASK_UTIL_EXPECT_* macros to retry and wait for test conditions verification
    Makes test more reliable
  Use TaskFire() to make test code run in any particular “scheduler task
  Test Parameterization
Sample unit test
  bgp_attr_test.cc
  bgp_mvpn_test.cc
  bgp_peer_close_manager_test.cc

## Slide 6: test driven development (tdd) Continued
bgp_stress_test – More of an integration test but still uses unit testing framework
  Wiki
  bgp_stress_test.cc
  E.g. build/debug/bgp/test/bgp_stress_test --pause --nevents=-1 --npeers=5 --nroutes=5 --nagents=5 --ninstances=5
  Introspect
Configuration load
  Load cassandra configuration directly into control-node like unit test
  E.g. DBLOG_DISABLE=1 CONFIG_JSON_PARSER_TEST_DATA_FILE=/cs-shared/db_dumps/workday.json CONFIG_JSON_PARSER_TEST_INTROSPECT=5910 controller/src/ifmap/client/testdata/cassandra_to_json.rb
  Introspect
  config_json_parser_test.cc
  cassandra_to_json.rb

## Slide 7: test driven development (tdd) Continued
Code coverage using gcov
  Sample Report for BGP
Profie using valgrind, zoom, etc.
  Sample interesting but that I found just last week while running an unit test